## Slide 1
Consultancy service for the Development of the Eastern Nile Water Resources Models and Tools
Nile Cooperation for Climate Resilience
Eastern Nile Technical Regional Office (ENTRO)
Training of Trainers in Eastern Nile Water Resources Models and Tools
HEC-DSSVue – Exercise 2
6 -10 May, 2025

## Slide 2
Introduction
This exercise demonstrates typical mathematical operations with HEC-DSSVue, computing reservoir inflow from gaged outflow and elevation data. It consists of two phases:
Data screening and estimating
Normalazing data (time series manipulation)
The data required for this workshop is located here:
    MathFunctions_1-2.dss

## Slide 3
Introduction
    The data sets and calculations used in this exercise are based on the gages and computational procedures used in support of regulation of the Corps' Lake Winnebago project. This shallow, glacially-formed lake covers approximately 214 square miles in east-central Wisconsin.
    The city of Fond Du Lac occupies the southern end of the lake. The Jefferson Park gage resides at the lake’s northern end in Menasha, where the lake flows out to form the Fox River. A gage located a couple of miles downstream at Appleton’s Lutz Park provides real-time outflows. The Fox River heads northeast for approximately 30 miles, passing through 7 low-head, run-of-river dams, until it empties into Lake Michigan at Green Bay.

## Slide 4
1.0 Part 1 - Introduction
Part 1
Data screening and Estimating
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 5
Many data sets contain erroneous values, which must be corrected before performing mathematical operations with the data. HEC-DSSVue provides some limited screening criteria, allowing values to be declared as 'missing', and/or quality flags to be set.
This workshop demonstrates three of the four mechanisms available to identify and replace invalid data:
Screen Using Minimum and Maximum
Screen with Forward Moving Average (not used in this workshop)
Manual editing of values inside Tabulation window
Estimate Missing Values
1.0 Part 1 - Introduction
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 6
Start HEC-DSSVue and open “MathFunctions_1-2.dss”
Select 'Condensed Catalog' under the View menu. In the absence of a time window, this makes subsequent operations on a pathname apply to all the records, regardless of the D-part.
Also under the View menu, ensure that the Unit System and Time Zone are rendered “As Stored”, in order to avoid inadvertent conversions when writing Math Functions results back to the database.
Select the data set named /FOX RIVER/LUTZ PARK/FLOW‑RES OUT//15MIN/USGS-CST/
Launch the Math Functions module under "Tools"
Plot and tabulate the data.
1.1 Select the data set
Notes: For multiple records, pathname parts that are the same for all records will show up in the dialog, while different parts (such as having pathnames with C parts of FLOW and STORAGE), will be displayed with an asterisk (*).

## Slide 7
1.1 Select the data set
Notes: For multiple records, pathname parts that are the same for all records will show up in the dialog, while different parts (such as having pathnames with C parts of FLOW and STORAGE), will be displayed with an asterisk (*).

## Slide 8
1.1 Select the data set
Note that the data contains many gaps and downward spikes. The station now has better technology, but this data was produced by a very old USGS Acoustic Velocity Meter. Each minute it made an instantaneous measurement of mean velocity across the channel, which it multiplied by cross-sectional area to calculate flow. Every 15 minutes it applied some very coarse quality-control procedures, averaged the samples, and reported the resulting flow to the USGS.
In situations where the actual data changes gradually, individual fluky values can be easily screened out using a “moving average” technique. However, this gage is located a short distance downstream of the Lake Winnebago outlet structures and hydropower facilities. Abrupt flow changes typically indicate gage malfunction but can be difficult to distinguish from actual variations due to gate movements or generating adjustments.
Notes: For multiple records, pathname parts that are the same for all records will show up in the dialog, while different parts (such as having pathnames with C parts of FLOW and STORAGE), will be displayed with an asterisk (*).

## Slide 9
1.2 Screen data
Open the Math Functions menu.
Choose the “General” tab
Set the “Operator” to “Screen with Forward Moving Average”:
  Your engineering judgment and experience with this gage suggest that the flows cannot realistically change more than 500 cfs in an hour.
  Screen the data set using the parameters shown in the figure.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 10
1.2 Screen data
Plot and tabulate your computed data to review the changes.
Try selecting 'Original Data with Computed' under the Display menu and re-plotting the data.
Question 1.
If the original curve covers up the “modified” curve in the plot, how can you switch order so that the revised curve is plotted on top of the original?
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 11
1.2 Screen data
Answer.
Go to the "Edit" button on the ribbon and select "Plot Properties..."
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 12
1.2 Screen data
Answer.
Use the arrows to the right to change the order of the curves
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 13
1.2 Screen data
In the “View" then "Quality” menu option of the tabulation, switch between “Symbol” and “Hex”.
  Note the three different quality flags associated with the “modified” data?
    “3” or empty cell means okay value,
    “5” or “M” means missing before the test
    “11” or “R” means rejected according to the test
Look again at the plot and note that many dubious values persist.
  The revised data is still unfit for use in computations.
  Perhaps a more aggressive screening test is needed.
  Leave the existing plot open for subsequent comparisons
Go back to the Math Functions window.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 14
1.2 Screen data
Choose “Restore Original Data” from the “Edit” menu, and verify that when you plot the data only the original pathname appears.
Verify that the “Screen with Forward Moving Average” Operator is still selected.
Leave the “Number To Average Over” at 4, but set the “Change Value Limit” to 200.
Click “Compute”.
Verify that 'Original Data with Computed' is turned on, and use the plot/tabulate functions to review the results
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 15
1.2 Screen data
Question 2.
Did the stricter test reject any additional bogus data?
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 16
1.2 Screen data
Answer
Yes. The point around the center of the data is not longer included in the screened data like it was in the screening attempt performed prior.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 17
1.2 Screen data
Question 3.
Did it reject any “good” data?
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 18
1.2 Screen data
Answer
Yes. We had some steep sudden changes in the data that were removed due to the screening.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 19
1.2 Screen data
Again Choose “Restore Original Data” from the “Edit” menu
Verify that when you plot the data that only the original pathname appears.
Screen the data set using the Minimum and Maximum screening function with the values shown in the figure below. Such specific parameters would not be suitable as generalized limits for automated processing, but represent the most effective parameters for the given period of this data.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 20
1.2 Screen data
Plot and tabulate your computed data to review the changes.
  Try selecting 'Original Data with Computed' under the Display menu and re-plotting the data
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 21
1.2 Screen data
Question 4.
Does the revised data set look ready for use in computations?
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 22
1.2 Screen data
Answer
Not ready yet because calculations (and models) generally require all values to be present. The missing values will need to be addressed in some way.
Also note the upward-spike on 9Oct2000, and a block of dubious data on 25Oct2000 still remain after the initial screening, so further clean-up is needed prior to estimating missing.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 23
1.2 Screen data
Using 'Save As', save your changes with a new F part of ‘USGS-CST-REV’, then close the Math Functions window.
From the main HEC-DSSVue screen, clear any previously selected pathnames, and tabulate your revised data.
From the tabulation window, enable the 'Allow Editing' option under the ‘Edit’ menu.
Scroll down to the values for 0703 and 0718 on 9Oct2000, and highlight the two rows.
  (NOTE: the times might appear as 0715 and 0730 due to a bug in some versions of DSSVue 3.0 that causes the times to be “snapped” to the top of the interval during the save to DSS).
Right-click on the selected values, and choose 'clear'. Save your changes to the same pathname, and close the tabulation window.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 24
1.2 Screen data
The spike down on October 25 is invalid and needs to be removed.
To accomplish this, set the time window in HEC-DSSVue to 0000-2300 on 25Oct2000
Select the recently created/revised data set and launch the Math Functions module again.
  This time the math operations are confined to data for 25Oct2000.
  Plot and tabulate the data to verify that flows below 4500 cfs are likely incorrect.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 25
1.2 Screen data
Run the 'Screen Using Minimum and Maximum' function again, with a Minimum Value Limit of 4500.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 26
1.2 Screen data
Save the data in the ‘USGS-CST-REV’ pathname again, and close the Math Functions screen
Clear the time window in HEC-DSSVue, and plot the data.
All suspicious values should be gone.
Close your plot.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 27
1.3 Estimate missing values
Select the same revised Lutz Park flows, launch the Math Functions module.
Choose the “General” tab and select “Estimate Missing Values” from the drop-down menu
Set the maximum consecutive number of missing to 96, so that it will not interpolate values if the missing values could span a complete day.
Press ‘Compute’.
Plot and tabulate the new data set, verifying that all of the missing values have been filled in.
Save your data.
Notes: When you delete data from a HEC-DSS file, the data is marked as missing but it is not actually removed from the file until you run a Squeeze of the file (will se in the next sections). You can recover deleted records with the Undelete command.
From the Edit menu, point to Undelete.
To undelete all records click All. A dialog box will appear to confirm that you want to undelete all of the records in the file. Click OK. A confirmation message will appear that states the records have been undeleted.
To undelete the records that you have just deleted click Last Deleted. A dialog box will confirm that you want to undelete the records that you just deleted. Click OK. A confirmation message will appear that states the records have been undeleted.
If you click Select, a list of the previously deleted pathnames will open. Check the boxes next to the records that you want to undelete, or click Select All to undelete all records in the list. You can unselect the checked records by clicking Unselect All. Once you have made your selection, click OK to undelete those records and close the dialog. Alternatively, you can click Apply to undelete the records and leave the dialog box open. A confirmation message will appear stating that the records have been undeleted.

## Slide 28
1.3 Estimate missing values
Notes: When you delete data from a HEC-DSS file, the data is marked as missing but it is not actually removed from the file until you run a Squeeze of the file (will se in the next sections). You can recover deleted records with the Undelete command.
From the Edit menu, point to Undelete.
To undelete all records click All. A dialog box will appear to confirm that you want to undelete all of the records in the file. Click OK. A confirmation message will appear that states the records have been undeleted.
To undelete the records that you have just deleted click Last Deleted. A dialog box will confirm that you want to undelete the records that you just deleted. Click OK. A confirmation message will appear that states the records have been undeleted.
If you click Select, a list of the previously deleted pathnames will open. Check the boxes next to the records that you want to undelete, or click Select All to undelete all records in the list. You can unselect the checked records by clicking Unselect All. Once you have made your selection, click OK to undelete those records and close the dialog. Alternatively, you can click Apply to undelete the records and leave the dialog box open. A confirmation message will appear stating that the records have been undeleted.

## Slide 29
1.3 Estimate missing values
Check the already existing record /FOX RIVER/LUTZ PARK/FLOW-RES OUT//15Minute/USGS-CST-FIXED/.
It is a “fixed” version provided by an experienced professional:
  It points out that the powerhouse really did have a hiccup on 25Oct2000
  The parameter type must be "INST-VAL" according to an arbitrary but long-standing convention
  Plot and tabulate your "-REV" data vs the "-FIXED" data.
Notes: When you delete data from a HEC-DSS file, the data is marked as missing but it is not actually removed from the file until you run a Squeeze of the file (will se in the next sections). You can recover deleted records with the Undelete command.
From the Edit menu, point to Undelete.
To undelete all records click All. A dialog box will appear to confirm that you want to undelete all of the records in the file. Click OK. A confirmation message will appear that states the records have been undeleted.
To undelete the records that you have just deleted click Last Deleted. A dialog box will confirm that you want to undelete the records that you just deleted. Click OK. A confirmation message will appear that states the records have been undeleted.
If you click Select, a list of the previously deleted pathnames will open. Check the boxes next to the records that you want to undelete, or click Select All to undelete all records in the list. You can unselect the checked records by clicking Unselect All. Once you have made your selection, click OK to undelete those records and close the dialog. Alternatively, you can click Apply to undelete the records and leave the dialog box open. A confirmation message will appear stating that the records have been undeleted.

## Slide 30
1.3 Estimate missing values
Question 5.
Does re-defining the parameter type to "INST-VAL" actually change anything?
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 31
1.3 Estimate missing values
Answer
Yes, the meaning of the timestep has changed. What was previously the end of an averaging period is now the time of an instantaneous observation.
Notes: To delete records from a HEC-DSS file:
Select the record or records to delete.
From the Edit menu, select Delete Records. A dialog box will confirm that you want to delete those records. If the number of data sets is four or less, their pathnames will be displayed in the dialog.
Click OK. A confirmation message will appear, stating that the records have been deleted.

## Slide 32
2.0 Part 2 - Introduction
Part 2
Normalazing data
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 33
After data sets have been screened, they may still require conversion to a common time-series scale before being used together in computations.
In order to calculate hourly reservoir inflow, the data sets for the lake levels and outflows should be normalized to the same hourly intervals.
2.0 Part 2 - Introduction
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 34
Clear any time window that may be set, select the data set named /FOX RIVER/LUTZ PARK/FLOW‑RES OUT//15MIN/USGS-CST-FIXED/
Launch the Math Functions module.
Set the ‘Selected Data Set’ field to the outflow pathname and tabulate the data.
  Note that the outflows occur every 15 minutes, at an offset of 3 minutes.
  Subsequent calculations require hourly flows averaged at the top of the hour.
Select the ‘Min/Max/Avg/…Over Period’ operator under “Time Functions”.
Select a "Function Type" of "Average over Period".
Set the time interval to 1HOUR.
Leave the offset box unchecked - the default is to use the end-of-period (i.e., “top of the hour”).
Click ‘Compute’
2.1 Convert to hourly intervals
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 35
Question 1.
Tabulate the new data set. What is the “Type” of the resulting data? How does this affect the values computed for the new time interval?
2.1 Convert to hourly intervals
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 36
Answer
The type of data generates is "PER-AVER" data. This impacts the computed results due to the fact that we are averaging the data over the period. Since this is an averaged value we will not peak as high as compared to the 15-minute data.
2.1 Convert to hourly intervals
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 37
Save your new data set using the suggested E-part of 1HOUR (this will be auto-generated due to the timestep).
2.1 Convert to hourly intervals
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 38
The two elevation data sets will later be averaged into a mean reservoir level, but first must be normalized to hourly data. The irregular Fond Du Lac data set consists of readings taken at the top of each hour, as well as one taken every 4 hours at the satellite ‘shoot’ time.
Clear any time window that may be set, select the data set named /LAKE WINNEBAGO/FOND DU LAC/ELEV//IR MONTH/COE CST
Launch the Math Functions module.
Set the ‘Selected Data Set’ field to the Fond Du Lac pathname and select the ‘Irregular to Regular’ Time Functions operator.
Select the “Interpolate” option.
Set the time interval to 1HOUR.
Leave the offset box unchecked - the default is to use the top of the hour.
Click ‘Compute’.
2.2 Interpolation
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 39
Tabulate the results to verify that only the top-of-hour values remain.
From the Math Function’s File men save the data set using the suggested E-part of 1HOUR.
2.2 Interpolation
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 40
The 30-minute Jefferson Park data set consists of instantaneous readings taken at 2 and 32 minutes past each hour. If simply converted to an hourly interval, the levels at the top of the hour would be linearly interpolated between the values at 32 and 2 minutes. This has the unfortunate effect of attenuating the high and low points. It is preferable to avoid this attenuation by extracting the 2-minute offset readings, and “snapping” them back to the top of the hour.
Clear any time window that may be set, select the data set named /LAKE WINNEBAGO/JEFFERSON PARK /ELEV//30MIN/COE-CST/
Launch the Math Functions module.
2.3 Snapping
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 41
Set the ‘Selected Data Set’ field to the Jefferson Park pathname and select ‘Irregular to Regular’ Time Functions operator.
Select the “Snap” option.
Set the time interval to 1HOUR.
2.3 Snapping
Check the ‘Tolerance Forward’ offset box and specify ‘2’ and ‘Minute’.
Click ‘Compute’
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 42
2.3 Snapping
Tabulate the results to verify that only the values originally at a 2-minute offset remain, and that they are now shown with an offset of 0 minutes.
Save the data set using the suggested E-part of 1HOUR.
Exit the Math Functions screen.
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 43
2.3 Snapping
From the HEC-DSSVue Main Window, tabulate the new hourly pathnames for Fond Du Lac, Jefferson Park, and Lutz Park to verify that all the data occurs at the top of the hour.
  (NOTE: the Jefferson Park times might appear still offset by 2 minutes due to a bug in some versions of DSSVue 3.0 during the save to DSS. If this is the case, proceed using the pathname “/LAKE WINNEBAGO/JEFFERSON PARK/ELEV//1Hour/COE-CST-FIXED/” or operate a Shift in Time operation)
Notes: The duplicate command in the Edit menu duplicates records in the same HEC-DSS file, giving the new records different pathnames.
Select the record named /GREEN RIVER/OAKVILLE/STORAGE/22Apr1992 - 21May1992/1HOUR/OBS/
From the Edit menu, select Duplicate. The New Pathname Parts for Duplicate Records dialog box will open (Figure 2‑2).
Parts A, B, C and F boxes be change based on your new choice, you cannot change the D or E parts for time series data.

## Slide 44: Thank You
Notes: Click on the graphical edit button.
Press the Single-Point Edit tool.
Find the new value of the point on the graph that you want to edit and double click the mouse at that location. A magenta triangle will appear in that location and a value will appear in the corresponding row in the estimate entry column.
Press the curve edit tool
Draw a curve in the graph (right click for the final point). A series of magenta triangles will appear in the new desired values and simultaneously the corresponding Estimate/Entry cell will be modified.
Press the Accept button or the Accept All button to accept all edits. This will copy the data from the Estimate/Entry column into the Revised column.
At the end of all of your edits, press the Save or Save As button.