## Slide 1
Consultancy service for the Development of the Eastern Nile Water Resources Models and Tools
Nile Cooperation for Climate Resilience
Eastern Nile Technical Regional Office (ENTRO)
Training of Trainers in Eastern Nile Water Resources Models and Tools
HEC-DSSVue – Exercise 1
6 – 10 May 2025

## Slide 2
PART 1
Basics of HEC-DSSVue
EXERCISE
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 3
Open the DSS file dssclass.dss.
There are three main catalog views in DSSVue: Pathname List, Pathname Parts, and Condensed Catalog. These catalog options are available under the View menu and can be selected one at a time.
By default, each catalog view will display a list of record pathnames sorted in ascending alphanumeric order (by A, B, C, D, E, and F Parts).
The No Pathnames and Unsorted List options are used (rarely) to access very large databases using scripted functions. Sorting large catalogs can take time, and there is the potential of running out of sort memory, so these options allow access to the file without sort problems.
Task 1. Cataloging Files and Searching for Records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 4
From the View Menu, switch between the options “Pathname List”, “Pathname Parts”, and “Condensed Catalog”.
In each catalog view, browse the list of displayed DSS records using the scroll bar to get a general idea about the assortment of pathnames in this particular DSS file.
Test the search options from the View menu to filter the list of pathnames by String or by Parts. (For Instance, in the Pathname Parts view, filter the list of pathnames to only show one pathname: /MYRIVER/DAVIS/FLOW/18NOV2001/IR-DAY/CDEC_INCOMING/)
Try sorting DSS records within each catalog view by clicking on different headers of the DSS records. (For Example, in the Condensed Catalog view, click on the “C Part” header to sort the DSS records by C Parts. Or click on the “F Part Header” to sort records by F Parts.)
Task 1. Cataloging Files and Searching for Records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 5
Question 1.
List one or two distinctive differences in the display of pathnames among the catalog views of DSS records.
Task 1. Cataloging Files and Searching for Records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 6
Answer
Pathname List – no columns to separate the pathname parts – parts are delimited by /s
Pathname Parts – columns are used to separate the pathname parts
Condensed Catalog – displays a shorter list than Pathname Parts because the D parts are compressed into a “range” (for records whose other pathname parts are all the same)
No Pathnames and Unsorted List – used for (very) big DSS files which are slow to catalog and sort.
Search …by string – a single field is displayed to allow you to enter a filter string. Wildcards are implied. For example – if you just enter “flow”, every pathname that includes flow ANYWHERE in the pathname will be listed.
Search …by parts – six dropdown boxes are displayed allowing you to selected filters by pathname parts. The dropdowns include each unique string that is used by the pathnames in the current dss file.
Task 1. Cataloging Files and Searching for Records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 7
Question 2.
For A Part = YOUR BASIN, B Part = LOOKOUT POINT, C Part = FLOW-RES IN, E Part = 1DAY, F Part = BASE3, determine the number of records whose pathname references in the Pathname Parts view was reduced to a single line reference in the Condensed Catalog view
Task 1. Cataloging Files and Searching for Records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 8
Answer
32.
The View-Condensed Catalog combines 32 different D parts into a single string '06Jan1936 - 31Dec1999'
Task 1. Cataloging Files and Searching for Records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 9
Question 3.
Search for pathnames with D Parts that contain the year 1945. Which catalog view did you search in? What type of search did you carry out? How many pathnames were filtered by your search?
Task 1. Cataloging Files and Searching for Records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 10
Answer
5.
Searching with 'Search pathnames by string' allows searching for '1945'. This works with all catalogs except (no pathnames, and condensed catalog).
Note: visually verify the string 1945 does not occur in other than the D parts.
Task 1. Cataloging Files and Searching for Records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 11
Open the DSS file Sample.dss and select the Condensed Catalog view.
A single DSS record or multiple DSS records listed in the main DSSVue window can be plotted and/or tabulated by using the Plot and Tabulate options in the Display menu or using the shortcut buttons in the tool bar menu (for plotting, and for tabulating).
1.2 Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 12
1. Plotting a single record.
Highlight any row in the list of pathnames.
Double click on the row, or alternatively press the Select button at the bottom of the main DSSVue window. The complete pathname should appear in the Selected Records section of the main window.
Try plotting and then tabulating. Separate windows should pop up, one for the plot and another for the table.
The plot and table windows can be closed when they are no longer of use.
In the main DSSVue window, deselect the pathname in the Selected Records section by highlighting and then pressing the De-Select button at the bottom of the main window.
Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 13
2. Plotting multiple records at the same time.
Highlight, Select, and Plot two non-consecutive rows from the list of pathnames that have different C Parts:
/GREEN RIVER/GLENFIR/FLOW/01APR1992 – 01MAY1992/1HOUR/EDIT/
/GREEN RIVER/OAKVILLE/ELEVATION/01MAY1992/1HOUR/OBS/
You can highlight and select one row at a time. Or you can highlight the two different rows at the same time with the left mouse button while holding down the CTRL key, then press the Select button to select the pathnames simultaneously.
Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 14
Plotting multiple records at the same time.
Once the pathnames are selected, plot their associated records.
The resulting plot should contain two viewports for the different records, as well as a legend. Notice that as a default setting within the plot, the viewports have the same weight in area.
Changing the relative sizes of viewports in a plot as well as other wide-ranging customizations of plots, such as customizing axes and adding titles, are possible in DSSVue.
Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 15
3. Drag the following pathname on to your plot: /GREEN RIVER/ OAKVILLE/STORAGE/01MAY1992/1HOUR/OBS/.
With your mouse, highlight the pathname. Do this by single clicking it.
Release the mouse button. Now click it again and hold down the mouse in the highlighted pathname. Move your mouse, without lifting up the button, to the plot. Release when you are on the plot.
It can take some time to get the hang of selecting and dragging in Windows.
Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 16
For this workshop, try out the zoom tool. In addition to enlarging sections of the plot, you can move the zoom tool over a curve, which will pop up a text box with the date and value of the point on the curve you are pointing to.
Tabulate these multiple records by using the Table button from HEC-DSSVue.
You can customize the resulting table’s display from the View menu by choosing to show Commas in tabulated numbers and selecting the number of Decimal Places you wish to display.
You can also show the Date and Time Separately and display the Date with 4 Digit Years as opposed to the default setting that shows the date and time in one column and displays the date with 2-digit years.
Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 17
Click on the Set Time Window button at the bottom right-hand corner of the main DSSVue window.
Limit the time window to the month of May 1992.
Press OK and notice the bottom prompt of the main DSSVue window, which will indicate the specified time window.
Re-plot and tabulate the selected record data, which would only span the specified time window.
When finished, you can clear the time window by pressing the Clear button in the Set Time Window
Task 2. Plotting and Tabulating data
5. Try setting a time window for these multiple records for plotting and tabulating.
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 18
Question 5.
Select the following pathname:
/GREEN RIVER/OAKVILLE/FLOW-RES OUT/01MAY1992/1HOUR/OBS/
and determine how many data values are stored in this record?
Are there any missing values?
What is the maximum reservoir release and when does it occur?
Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 19
Answer
One way to investigate the data is to tabulate, then click on the value column to sort. Click a second time to sort High to Low.
Max value is 8,000 cfs
There are 504 data values.
Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 20
Reset the time window back to No Time Window. Keep working with the DSS file Sample.dss.
A Plot can be printed, saved as an image format, or copied to the system clipboard and placed in other applications such as Microsoft Word and Excel.
A Table can likewise be printed, exported and saved as an external file, and contents of a table can be copied and pasted directly into other applications such as Microsoft Word and Excel.
Task 3. Copying Plots and Tables for use in other programs
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 21
Select any pathname and Plot.
Select the Print Preview option from File menu and close the preview after you glance at it.
Save the plot in *.JPEG format with the Save As option in the plot’s File Save the image to the workshop directory
Task 3. Copying Plots and Tables for use in other programs
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 22
Generate a Table by selecting Tabulate from the File menu in the plot window
Use the View menu to cause the date and time to be in separate columns.
Highlight a portion of the table by holding down on the left mouse button and dragging the mouse over the area to be selected.
Right-Click on the highlighted cells and, from the context menu, select the Copy option (or select the Copy option from the table’s Edit menu).
Paste the data in an MS Excel sheet.
Task 3. Copying Plots and Tables for use in other programs
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 23
Open the DSS file dssclass.dss.
In DSSVue, record data can be copied in a couple of ways:
  Records can be copied from one DSS file to another DSS file or duplicated within the same DSS file.
  Record Pathnames can also be renamed or deleted within a DSS file.
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 24
Copy a record to another DSS file:
Highlight and then Select the record pathname /SHASTA/DELTA/STAGE-FLOW///CDEC-WEB/.
Choose the Copy To option in the Edit (A Copy Records into HEC-DSS File dialog should appear.)
Browse to the workshop directory ……/Overview of HEC-DSSVue
Create a new DSS file by typing a new file name MyWorkshop.dss in the File Name field of the dialog, then press Open.
Open your new HEC-DSS file and verify that the data has been successfully copied to the DSS file you specified. The file you open should show up in a new tab.
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 25
Question 6.
Try copying a record from a DSS file into the same DSS file.
What do you expect to happen?
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 26
Answer
A warning indicates records with the same name will be overwritten.
Task 2. Plotting and Tabulating data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 27
Select the dssclass.dss tab.
Copy the remainder of the SHASTA records by dragging them onto the MyWorkshop.dss tab.
With your mouse, highlight the other three SHASTA pathnames.
Do this by single clicking on the first and then hold down the Shift key and clicking on the third pathname.
Release the shift key and mouse button.
Now click and hold down the mouse in the middle of the highlighted pathnames.
Move your mouse, without lifting up the button, to the MyWorkshop.dss tab.
Release when you are on the tab.
  Which pathnames are highlighted may change when you are moving your mouse, but they should resort when you get to the tab (or anywhere off that part of the window.)
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 28
Question 6.
What happened when you did this?
Answer
The records are copied to myworkshop.dss
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 29
Duplicate the pathname /YOURBASIN/11419000/FLOW/01JAN1903/1DAY/HYDROCD/.
Highlight the pathname and right click and select Duplicate from the popup menu.
You will be prompted with a dialog where you can change the pathname.
Change the B Part from “11419000” to “USGS GAGE” and press OK.
The catalog should refresh automatically.
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 30
Question 7.
There are 44 record pathnames where the B Part=11419000.
What is an easy way to duplicate all 44 records and change the B Part to USGS GAGE?
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 31
Answer
Before using the duplicate command, first change the catalog view to be condensed catalog. This way all records in the data set are copied together.
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 32
Rename all pathnames with A Part “YOURBASIN” to “YOUR BASIN”.
Select all the pathnames with A Part=YOURBASIN
Apply the Rename option in the Edit Or just right-click the pathname and select Rename.
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 33
Question 8.
What do asterisks that appear in the B Part and F Part fields indicate?
Answer
The asterisks '*' indicates match and re-use the existing Part names.
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 34
Question 9.
If a record pathname were in the Selected Records section, and another record pathname was only highlighted in the Pathname List, then the Delete option is applied, which record will be deleted?
Answer
Only the records selected in the Selected Records Section.
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 35
Delete the 44 records you duplicated earlier with B Part=USGS GAGE.
The Delete Records option is under the Edit menu.
Note that after you have deleted the records you can restore them by applying the Undelete -> Last Deleted option under the Edit menu.
The Undelete -> Last Deleted option will only restore the most recently deleted records.
The Undelete option will NOT restore deleted files after the Squeeze option, which removes inactive space in a DSS file, is applied from the Tools menu.
Task 4. Copying, duplicating, renaming, and deleting existing records
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 36
PART 2
Graphics Capabilities
EXERCISE
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 37
Start HEC-DSSVue.
Open the sample.dss file.
Select Pathname Parts from the View menu.
Filter the pathname list for records containing data for Jan 2002 by selecting the 01Jan2022 in the D part filter dropdown list.
Filter the pathname list further or sort the pathnames by the B or C part by clicking the header of the desired column to find the following three records and add them to the selection list by either double-clicking the records or by highlighting all of them and pressing the Select button.
//DEWEY-LAKE/ELEV/01JAN2002/1HOUR/OBS/
//DEWEY-LAKE/FLOW/01JAN2002/1HOUR/OBS/
//DEWEY-LAKE/PRECIP-INC/01JAN2002/1HOUR/OBS/
Task 1. Creating a Plot
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 38
Plot them by selecting the Plot button on the tool bar.
Open the View menu to make sure that Use Line Styles is not selected (off) on the plot (there should not be a checkmark in front of the Use Line Styles entry in the menu)
Task 1. Creating a Plot
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 39
Question 1. How many viewports are on the plot?
Answer
3
Question 2. What color is the elevation curve?
Answer
Blue
Question 3. What color is the elevation curve?
Answer
Green
Task 1. Creating a Plot
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 40
Reconfigure the plot layout.
Select Configure Plot Layout from the plot's Edit menu.
Make adjustments so that the precipitation curve is plotted in the top viewport by highlighting the precipitation viewport in the Selected Data Sets and clicking the up arrow.
Move the elevation and flow curves to the bottom viewport by highlighting the Left Y Axis holding the flow curve and moving it to the elevation curve's viewport in the same way.
The elevation and flow should be plotted in the same viewport, with elevation on the left.
Task 2. Configuring the Plot Layout
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 41
Invert the axis of the precip curve by right clicking the axis with the pointer, selecting Edit Properties, and selecting the Reverse (Invert) Axis box.
Adjust the size of the viewports such that the top viewport is about ½ the size of the bottom one by selecting Edit and Configure Plot Layout.
  Change the size of each viewport by selecting Set Plot Viewport Weights from the Edit menu of the Configure Plot dialog. The weights you enter are in percentages of the total area of the plot.
Task 2. Configuring the Plot Layout
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 42
Adjust the Y-axis of the elevation curve to range from 645 to 647 and the Y-axis of the flow curve to range from 0 to 2000 by right clicking the axis and selecting Properties then adjust the min and max values.
Open the Axis Properties editor by right-clicking on the axis and selecting Edit Properties.
Task 2. Configuring the Plot Layout
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 43
Add fill to the precip curve by right clicking on the precip curve in the viewport and selecting Edit Properties from the context menu.
Modify the plot properties of the other curves by changing their line characteristics (color, style, weight, symbol, etc).
Question 8. Which option for "fill:" made the most sense on the precip curve? Why?
Answer
"Above", because it fills from zero to the precip value.
Task 2. Configuring the Plot Layout
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 44
Save a template of this plot to be applied later to another plot using Save Template from your plot's File menu
Close your plot.
Re-plot the selected records.
Apply your template to the new plot by selecting Apply Template from your plot's File menu, then selecting the template you saved in previous step.
Task 2. Configuring the Plot Layout
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 45
Add an icon to one side of the default legend so that any plot you produce will contain the icon and text
Select Default Plot Properties from your plot's Edit menu
Select the Legend tab
Choose either the Right or Left block tab
Select the Draw Legend Block checkbox
Then add your icon.
  Valid icon file types include .jpg, .gif, .bmp, and .png.
Task 3. Edit Default Plot Properties
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 46
Create a new plot with at least 4 flow records displayed utilizing the steps previously outlined.
Check the plot's View menu to make sure that Use Line Styles is "on".
Task 3. Edit Default Plot Properties
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.