## Slide 1
Consultancy service for the Development of the Eastern Nile Water Resources Models and Tools
Nile Cooperation for Climate Resilience
Eastern Nile Technical Regional Office (ENTRO)
Training of Trainers in Eastern Nile Water Resources Models and Tools
SWAT
6 – 10 May 2025

## Slide 2
1.1 SWAT OVERVIEW
Install QGIS by running https://www.qgis.org/download/ (or later version)... It can be downloaded from the QGIS download page, where you should select the most stable version LTR.
Install SWAT+ by running swatplustools-installer, version 3.0 or later. It can be downloaded from SWAT+ page https://swat.tamu.edu/software/plus/ . You may be informed that Windows protected your PC, and you need to click More info and then Run anyway to proceed with the installation. You then need to accept the license. This is a combination installer that provides QSWAT+, the SWAT+ Editor, and some other materials. You can choose which components you need (for the first install QSWAT+, the SWAT+ Editor, probably the global weather generator, and the SSURGO/STATSGO soil data if you will be modelling anywhere in the USA)
Setting up Q-SWAT+
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 3
1.1 SWAT OVERVIEW
The directories created in the SWATPlus directory are:
SWATPlusEditor containing the editor and the SWAT+ program
Databases containing a template project database, a reference database, a template project file, the global weather generator database (if selected for Windows) and the SSURGO/STATSGO soil database (if selected for Windows).
Documents containing the SWAT manual (if selected in the Windows QSWAT+ installer,always for Linux and Mac)
ExampleDatasets containing the Robit example used in this presentation
TauDEM539Bin containing the TauDEM programs used in watershed delineation.
Tools containing
  ConvertFromArc containing a converter from ArcSWAT projects to QSWAT+ projects.
  SWATGraph (optional in Windows installer)
Directories intsalled
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 4
1.1 SWAT OVERVIEW
The example files used in this manual are available in the SWATPlus directory
in a directory ExampleDatasets/Robit. This directory contains:
DEM in directory DEM
stream reaches file to burn into the DEM, in directory RobitStreams
An outlet file in directory MainOutlet
Landuse and soil maps in directories Landuse and Soil
Climate data in directory ClimateRobit
Some csv files for making database tables, and
An observed data file observedFlow.csv in directory Observed.
Structure and Location of Source Data
Notes: The U.S. Army Corps of Engineers’ Hydrologic Engineering Center Data Storage System, or HEC-DSS, is a database system designed to efficiently store and retrieve scientific data that is typically sequential.

## Slide 5
1.2 SWAT SETUP
Installing the QSWAT+ plugin
Start QGIS and select Plugins menu -> Manage and Install Plugins and find QSWATPlus.
If you already have an older version QSWATPlus3_12 (or 3_9 or 3_64) uncheck it first.

## Slide 6
1.2 SWAT SETUP
Installing the QSWAT+ plugin
Click the QSWATPlus checkbox to install, which takes a few seconds.
The QSWAT+ icon will appear in the toolbar.

## Slide 7
1.2 SWAT SETUP
Starting QSWAT+
Start QSWAT+ by clicking the QSWAT+ icon.
The main QSWAT+ interface will be displayed

## Slide 8
1.2 SWAT SETUP
QSWAT+ Parameters
Click the QSWAT+ Parameters button
If you installed the SWAT+ Editor and datasets somewhere other than the default directory, you can change it.
MPI is the Message Passing Interface which QSWAT+ can use for different watershed delineation. It is not essential, and if you don't want to install it you can uncheck Use MPI.
There are a number of other parameters you can set, mostly for fine tuning your model, and beyond the scope of this introduction.
If you have changed anything, click Save, else Cancel.

## Slide 9
1.2 SWAT SETUP
Starting a new project
In the main QSWAT+ form click the box New Project.
A browser will be displayed requesting a parent directory for the new project. Browse to a folder such as C:\QSWATPlus_Projects.
You will need to create the folder Robit. Select it so it appears in the text box below and click Select Folder.
A new form opens asking for the project name, which must start with a letter. Type in Demo and click OK.

## Slide 10
1.2 SWAT SETUP
Starting a new project
The interface now presents a step-by-step configuration to be followed in order to prepare theSWAT+ simulation, starting with Step 1 (Delineate Watershed)
Note that it displays the path of the project folder at the foot.
At this stage all your maps should be prepared in an equal area projection (probably, but not necessarily, UTM).
All the maps should be in the same projection coordinate system.

## Slide 11
1.3 WATERSHED DELINEATION
We are now ready to take the first step in running QSWAT+. Our main form indicates that we will first Delineate Watershed.
Click this button to open the watershed delineation form.
The purpose of watershed delineation is to identify
where the streams and channels will run
which parts of the area will drain into which reaches of the streams: these are subbasins
(optionally) which parts of the area are classified as floodplain or upslope.
A reach of a stream is a portion between two stream junctions, or from a source to a junction, or from a junction to the main outlet.

## Slide 12
1.3 WATERSHED DELINEATION
Watershed delineation form

## Slide 13
1.3 WATERSHED DELINEATION
Loading the DEM
The first task in watershed delineation is to load a digital elevation map (DEM).
Digital elevation maps are grids (also called rasters) in which the value at each point is the elevation (height above sea level), commonly in metres.
QSWAT+ accepts a wide range of grid formats, in fact any format acceptable by the Geospatial Data Abstraction Library (GDAL)
QSWAT+ uses TauDEM (http://hydrology.usu.edu/taudem/taudem5/) to do the watershed delineation, and TauDEM requires GeoTiff format DEMs. So if necessary QSWAT+ does a conversion to GeoTiff when it copies the DEM into the project.
Watershed delineation, and later modeling by SWAT+, assumes that each cell in the DEM grid represents the same area. So the DEM needs to be projected into, for example, UTM. (UTM is not exactly an equal area projection, but is close enough for most purposes.) So if your DEM is in lat-long projection you will need to use the tools of QGIS to reproject it before you use it in QSWAT+. (Use the menu item Raster, then select Projections and Warp (Reproject)

## Slide 14
1.3 WATERSHED DELINEATION
Selecting a DEM
Click the Select DEM button to open the Select DEM form, and navigate to Robit\DEM.
In this example we have an ESRI grid, which is stored in its own directory srtm_30m .
The GDAL convention for ESRI grids is to select the hdr.adf file as the one to load. (Pull down the list currently set to All files to see the conventions for other grid formats.) Select hdr.adf and click Open.

## Slide 15
1.3 WATERSHED DELINEATION
Selecting a DEM
As the DEM is converted to GeoTiff you may briefly see the shell window where GDAL is working. Then the DEM is displayed in QGIS
A Hillshade layer is also created to give a better impression of the terrain.

## Slide 16
1.3 WATERSHED DELINEATION
DEM properties
If you select the DEM properties tab in the Watershed Delineation form you can see information on the horizontal and vertical units, the cell size, the area of a cell, the extent, and the projection.
If your DEM has vertical units other than meters this is the time to select the units.

## Slide 17
1.3 WATERSHED DELINEATION
Setting the thresolds
Return to the Delineate watershed tab.
There is an option to burn in an existing stream network. This is useful when you have a suitable map to use and all or part of your area is relatively flat. It lowers the DEM elevations along the streams so that delineation can find them.
We have one for this example: check Burn in existing stream network and navigate to Robit\RobitStreams\robReach.shp. Click Open. This file is added to the map canvas.

## Slide 18
1.3 WATERSHED DELINEATION
Setting the thresolds
Delineation needs a number representing the minimum area needed to form a stream and to form a channel. These can be defined as either a number of cells or as an area, and you can choose the units to use for an area.
Default values are already provided.
You can use these, create the channels and streams, change them and create them again, until what you get looks reasonable.
We will change the units to hectares, and put 9 ha as the area for a channel and 90 ha for a stream. The number of cells changes to 100 and 1000 (as the DEM cells are 30 metres square.)

## Slide 19
1.3 WATERSHED DELINEATION
Setting the thresolds
The threshold is the number of cells (or area) required to form a channel or a stream: a cell will be made part of a channel or stream if it has at least the threshold number of cells draining into it.
Stream reaches are sections of the stream network between significant points, where significant points are stream sources, monitoring points like water gauges, stream junctions, inlets, and watershed outlets.
A subbasin is an area draining into a stream reach. Subbasins are the main divisions of the watershed, and typically the entities whose SWAT outputs we will want to generate and study.
Channels are finer divisions and extensions of stream reaches, and allow us to place more precisely the components of the watershed which will form the SWAT+ model: landscape units, reservoirs, ponds, point sources, and hydrological response units.

## Slide 20
1.3 WATERSHED DELINEATION
Channel and stream definition
Click Create streams.
A series of TauDEM tools are run: PitRemove, D8FlowDir, DInfFlowDir, Area D8, AreaDinf, GridNet, Threshold, and StreamNet. You can examine their output in the Taudem output tab if you wish.
The channel and stream reach network is added to QGIS.

## Slide 21
1.3 WATERSHED DELINEATION
Defining outlets
We normally define at least a main outlet for our watershed.
It is also possible to define:
inlets, which we use if we want to model a large watershed in sections. QSWAT+ will exclude the area upstream from an inlet from its model.
upstream outlets, where SWAT+ will produce data, so we place these where we have measured data
reservoirs and ponds
point sources
You can define main outlets on more than one part of the stream network, to model the watershed in more than one piece. An outlet is 'main' if it has no outlet downstream from it.
If you don't use an inlets/outlets shapefile (also called a vector file), main outlets will be defined where the streams cross the edges of the DEM.

## Slide 22
1.3 WATERSHED DELINEATION
Defining outlets
Each inlet or outlet point you define will create a subbasin boundary, because it will define the end of a stream reach. Each reservoir, pond or point source you define will divide its channel into two channels.
It is possible to define points by using an existing shapefile or by drawing them interactively. Drawing them interactively will create a shapefile which we would use in future runs on the same project.
It is also possible to draw on an existing shapefile to create additional points, or to select only a subset of points in an existing shapefile.
All inlet or outlet points must be placed on a stream, and others on a channel, so if we want to do any drawing we need to display the channel and stream network.

## Slide 23
1.3 WATERSHED DELINEATION
Drawing points
We have a prepared outlet point file for this example, but first we illustrate how to draw points.
Make sure that Use an inlets/outlets shapefile is checked, and click on Draw inlets/outlets.
The Inlets/outlets form appears. Make sure that Outlet is selected, and click on the map around 328500, 1289500 Try to get the point on the stream. Click OK.

## Slide 24
1.3 WATERSHED DELINEATION
Snap threshold
If you zoom in you can see the point is almost certainly not exactly on the stream.
QSWAT+ will snap (move) points to the nearest channel or stream provided they are within the snap threshold, which defaults to 300 metres.
When we create the watershed, the form will say how many points were snapped. If this is less than intended we can use QGIS to move them closer, or just try increasing the threshold. If we have several points and some were not snapped (or to check in advance before creating the watershed), the Review snapped will show which have been snapped successfully.

## Slide 25
1.3 WATERSHED DELINEATION
Watershed creation
We will use an existing file containing our outlet. Right click on the Drawn inlets/outlets item in the Layers panel, and select Remove.
Click the button on the right of the Watershed Delineation form showing the inlets/outlets file, navigate to Robit\MainOutlet\MainOutlet.shp and Open.
Click Create watershed, and check that 1 snapped is reported on the Watershed Delineation form.

## Slide 26
1.3 WATERSHED DELINEATION
Watershed creation
Watershed creation reruns some TauDEM programs (AreaD8, GridNet, Threshold, StreamNet) and then produces and displays the watershed shapefile, showing the subbasin boundaries.

## Slide 27
1.3 WATERSHED DELINEATION
Creating landscape units (LSUs)
In QSWAT+ it is possible to divide subbasins into landscape units.
Two landscape units are possible, floodplain and upslope.
If we define landscape units, when we later come to define hydrological response units (HRUs) these will be defined within each landscape unit, and if we also choose to select only some HRUs, then each landscape unit will be treated separately, so that each landscape unit contains at least one HRU.
To define landscape units, we click the Create landscape tab and then the Create button. This brings up the Landscape analysis form

## Slide 28
1.3 WATERSHED DELINEATION
Creating landscape units
There are three methods of creating floodplains: buffering channels, DEM inversion, and branch length calculation.
Buffering channels is a simple method of creating a strip either side of the channel that is a multiple of its width (which QSWAT+ estimates from the area draining into it)
DEM inversion involves finding ridges by, effectively turning the DEM inside out and finding ridges as if they were streams. The floodplain consists of those points for which the ratio of a point's height above the stream to the ridge's height above the stream is at most the slope position threshold, which defaults to 0.1.
Branch length defines ridge points as those for which the length of flow path for an adjacent point to where the flow paths of the two points meet exceeds a threshold. It then uses slope position like DEM inversion.

## Slide 29
1.3 WATERSHED DELINEATION
Creating landscape units
Since it is not clear what method will be best for any particular watershed, the choice needs to be made by the user, and is probably best made visually.
For this exercise you should create the same three floodplain rasters. Click Done to close the Landscape analysis form.

## Slide 30
1.3 WATERSHED DELINEATION
Merging subbasins
Delineation often produces very small subbasins where there are small distances between stream junctions.
In QSWAT+ users can select and merge subbasins. This is especially important in avoiding small subbasins. To merge subbasins, select the option Select subbasins in the Merge subbasins tab. Hold the Ctrl key and click in subbasins you want to select. Selected subbasins will turn yellow, and a count is shown at the bottom left of the dialogue window
For the sake of this exercise, we will not merge the selected subbasin. Release the Ctrl key and click on the map outside the watershed and the selected subbasin will be unselected.

## Slide 31
1.3 WATERSHED DELINEATION
Merging subbasins
Checking the option of Select small subbasins provides the option to merge subbasins below a certain threshold (i.e. either the area in hectares or a percentage of the mean subbasin area)
For this exercise click the radio button percentage of mean area, and leave the default figure of 5 in the box next to it. Click Select.

## Slide 32
1.3 WATERSHED DELINEATION
Merging subbasins
It will show you subbasins that have an area less than 5% of the mean area.
When finished click “Save” to save your selection, or “Cancel” to abandon your selection.
You click Merge to perform the merge.
Note: You cannot merge a subbasin that has an outlet or inlet at its exit. So in this example, the only small subbasin is the one at the watershed outlet, which cannot be merged, and QSWAT+ will report this.

## Slide 33
1.3 WATERSHED DELINEATION
Delineation complete
The third tab in the delineation form is to Add Lakes. We have no lakes to add in our Robit example, and it is a substantial topic, so we will return to it later.
To complete watershed delineation you need to click OK. This calculates and saves information about the watershed, with the message Constructing topology, and causes the subbasins to be numbered.

## Slide 34
1.3 WATERSHED DELINEATION
Delineation complete
This step ends watershed delineation, and enables the Create HRUs option

## Slide 35
1.4 HRU definition
HRU definition
SWAT+ uses subdivisions of landscape units (LSUs) called hydrological response units (HRUs).
Each HRU is a particular combination of LSU, landuse, soil, and (optionally) slope range.
We have identified our subbasins, so the next step is to add landuse and soil information.
Our main form shows that Step 1: Delineate Watershed is done. We click Step 2: Create HRUs and we get a new form: Create HRUs.

## Slide 36
1.4 HRU definition
Adding landuse and soil data
To select the landuse map, we click on the button to get the Select landuses file form. In this case it is again an ESRI grid and so we navigate to Robit\Landuse\roblandusenew and select the hdr.adf file
Similarly we select the soil map, also an ESRI grid, from Robit\Soil\mowr_soil90 and select the hdr.adf file
You may notice that the landuse map is loaded as selected, as an ESRI raster with a name hdr.adf. But the soil map, instead of being mowr_soil90/hdr.adf is called mowr_soil90_clip.tif
This is because QSWAT+ checks to see if landuse and soil maps are substantially bigger than the DEM (at least 10 DEM pixels in any direction) and if so clips them to avoid loading a larger map than necessary.
So when preparing such maps for QSWAT+ you need to make sure their projection matches the DEM, and that they easily cover the watershed area, but do not worry about clipping them to size

## Slide 37
1.4 HRU definition
Lookup tables for landuse and soil
The landuse and soil maps are just grids of numbers. We have to relate these numbers to landuse codes and soil names, which we do by defining lookup tables in the project database. We can define these tables before we start, but for lookup tables there is an option to import comma-separated value (csv) files.
In the pull-down menus for Landuse table select Use csv file. Navigate to Robit and select Robit_landuses.csv. A table called Robit_landuses is created in the project database and appears as the Landuse table. Next time we run the project it will be available and selected when we start this form: we only need to read the csv file once (though we can change it and import it again).
Similarly, import Robit\Robit_soils.csv to make the soil lookup table Robit_soils.

## Slide 38
1.4 HRU definition
Lookup tables for landuse and soil
Lookup tables for landuses:
have landuse in their names
map LANDUSE_ID values (values found in the landuse map you will use) to SWAT_CODE values (SWAT+ landuse codes, found in the crop or urban table in the reference database)
Lookup tables for soils:
have soil in their names
map SOIL_ID values (values found in the soil map you will use) to SNAM values (soil names found in the usersoil table in the reference database)

## Slide 39
1.4 HRU definition
Soil properties
Unless our project is in the USA and we are using SSURGO or STATSGO, we also need a table describing soil properties.
This traditionally has a name usersoil, or one including that name, and is typically to be found in the project database. These are the defaults currently in the form for the database and the table name.
The default global_usersoil in the project database is appropriate for the global soils maps from the FAO, but in this case, we will use a specific csv file.
Leave the default landuse and soil database selection as it is (the project database), make sure the Soil data option is set to usersoil, and select Use csv file in the Usersoil table pull-down menu. Open Robit/Robit_usersoil.csv to create and select the table Robit_usersoil.

## Slide 40
1.4 HRU definition
Creating potential HRUs
We will use one of the floodplain maps we created earlier, to divide our subbasins into landscape units. Use the pull-down menu labelled Select floodplain map (optional) to select the floodmap by inversion invflood0_10.tif
We can divide HRUs also according to slope bands.
We add an intermediate point for slopes (e.g. 10) to divide HRUs into those with average slopes in the range 0-10% and those with average slopes above 10%.
Type 10 in the Set slope bands box and click Insert. The Slope bands box shows the intermediate limit is inserted
(You can insert as many intermediate points as you wish by repeating the procedure. Use Clear to start again.)
We can also at this point define elevation bands. These are bands used for subbasins at high elevation affected by snow and ice. You set them by defining a minimum elevation: only subbasins whose maximum elevation exceeds this are given slope bands, and by defining how many bands to use. We do not need them for this example.

## Slide 41
1.4 HRU definition
Creating potential HRUs
We can also at this point define elevation bands. These are bands used for subbasins at high elevation affected by snow and ice. You set them by defining a minimum elevation: only subbasins whose maximum elevation exceeds this are given slope bands, and by defining how many bands to use. We do not need them for this example.
We will also generate a FullHRUs shapefile: click in the check box. Generating this file is optional, as it can take some time if there are many HRUs. If you intend to visualise HRU outputs after running SWAT+ then you need to generate this file.
The Read choice is set to Read from maps and is currently the only choice. In future runs of the example, provided we don't change the watershed delineation, the soil and landuse files, or the slope bands, we will be able to Read from previous run.

## Slide 42
1.4 HRU definition
Creating potential HRUs
Click Read. This will read data about the subbasins, LSUs and slopes from watershed delineation, plus landuse and soil data, and can take some time, especially if generating a FullHRUs shapefile

## Slide 43
1.4 HRU definition
Potential HRUs created
After reading the grids you will notice a number of changes to the QGIS display:
A Slope bands map has been created and added. This allows you to see where the areas of the two slope bands selected for this project are located. If no intermediate slope limits are chosen this map is not created.
the landuse and soil maps are loaded and labelled with landuse codes and soil names from the lookup table (This should happen but sometimes apparently QGIS does not recognize the range of values and they will not appear on the map. The SWAT model will consider anyway the two maps)
a Full LSUs map and Full HRUs map have been added showing the LSU and HRU boundaries

## Slide 44
1.4 HRU definition
Potential HRUs created
Shapefiles Full HRUs and Full LSUs have been created and added.
This allows users to see where in each subbasin the landscape units (LSUs) and potential Hydrological Response Units (HRUs) are physically located.
A landscape unit is the region draining into a channel reach, further divided into the floodplain and upslope regions if a floodplain raster is used. LSUs form single regions: they each form a single polygon.
An HRU is the collection of pixels within an LSU that share the same landuse, soil and slope range. HRUs typically form a collection of polygons.

## Slide 45
1.4 HRU definition
Potential HRUs created
We can use the Full HRUs shapefile to see our potential HRUs.
If you Open Attribute Table you can see:
Subbasin
Channel
Landscape
Landuse
Slope band
Area
% Subbasin
% Landscape

## Slide 46
1.4 HRU definition
Merging short channels
Channels with small LSUs (typically short channels) generate HRUs that contribute strongly to the processing time of SWAT+ but make little difference to the results, and so it is common to merge them.
There are typically many channels so this is an automatic process rather than a manual one.
To counter this there is an option to merge short channels into neighboring ones, by selecting a threshold either as a percent of subbasin or as an area in hectares, and recreating the channel network.
Use the slider in the Short channel merge group (or type in the box) to set the threshold at 2%, select the Re-merge short channels option and click Read again.
You will see the channel count and Full HRUs count decrease

## Slide 47
1.4 HRU definition
Ponds and reservoirs
Ponds and reservoirs may be added in 3 ways:
By adding lakes
By adding pond or reservoir points to the inlets/outlets shapefile in watershed delineation. These points will be snapped to channels, and will divide channels in two. Areas of landuse WATR in the adjacent LSU of the upper channel will be allocated to the pond or reservoir. (The adjacent LSU is the floodplain if used, else the channel's single LSU.) Users are warned if there is no such WATR area.
By setting the Reservoir threshold, which is the percentage of landuse WATR in the adjacent LSU of each channel needed to form a reservoir. For example, if this is set to 20%, then any channel for which landuse WATR is 20% or more of the adjacent LSU will become a reservoir. If the downstream channel is also a reservoir by this method, they are combined into a single reservoir. The default is 101%, effectively turning this mechanism off. (This watershed has no WATR areas and so no reservoirs or ponds could be formed, even if we reduced the reservoir threshold).

## Slide 48
1.4 HRU definition
Reports
Before you continue with HRU definition, if you look at the main QSWAT+ window you see that a new item Select report to view is available and you can choose to view just two reports at this point, which are the Elevation and Landuse and Soil reports.
The elevation report gives information about how much land is at each elevation from the lowest to the highest, both for the watershed as a whole and for each subbasin
The landuse and soil report lists the landuse, soil and slope-band areas for each subbasin. It also lists the areas, divided into landscape units if these are in use, for each channel reach.

## Slide 49
1.4 HRU definition
Preparing to create HRUs
Completion of reading from maps, or reading from previous run, enables the second HRUs tab in the Create HRUs form, and we select it. This will enable us to create the actual HRUs to be used in the project, usually a selection of the full HRUs

## Slide 50
1.4 HRU definition
Splitting and exempting landuses
We have two further options now available in the Create HRUs form: Split landuses and Exempt landuses.
Exempting landuses means marking them as not to be removed when we come later to remove small HRUs. For example, the FRST (forest) landuse could be exempted. Make this exemption.
Splitting landuses allows us to divide existing landuses. Suppose, for example, we know that 50% of the landuse AGRL (generic agriculture) in this area is actually CORN and 50% is TEFF. To do this, first select AGRL in the Select landuse to split pull down menu. This immediately raises a Select sub-landuse form. Select CORN and click OK. This completes the first line of the table. Click the Add sub-landuse button, select TEFF and click OK. This adds the second line. Click then Save edits and Save splits

## Slide 51
1.4 HRU definition
Creating HRUs
Subdividing the watershed into areas having unique land use, soil and slope combinations enables the model to reflect differences in evapotranspiration for various crops and soils. Runoff is predicted separately for each HRU and routed to obtain the total runoff for the watershed. This increases accuracy and gives a much better physical description of the water balance.
The user has a choice between making each LSU into just one HRU or dividing it into multiple HRUs through the Single/Multiple HRUs selection.

## Slide 52
1.4 HRU definition
Creating HRUs
The first two choices define just one HRU for each LSU: single choices:
Dominant landuse, soil, slope chooses the landuse with the biggest area in the landscape unit, the soil with the biggest area in the landscape unit, and the slope range with the biggest area in the landscape unit and uses them for the whole landscape unit.
Dominant HRU selects the largest of the potential HRUs in each landscape unit and makes its landuse, soil and slope range the ones chosen for the whole landscape unit.

## Slide 53
1.4 HRU definition
Creating HRUs
The other three choices are multiple choices. If one of these are chosen it is possible to reduce the number of HRUs by eliminating small ones and redistributing their area proportionately amongst the larger ones.
The option of Filter by land use, soil and slope, will ignore any potential HRUs for which the landuse, soil or slope is less than the selected threshold. The areas of HRUs that are ignored will be redistributed proportionately amongst those that are retained within each landscape unit.
The option of Filter by area will ignore HRUs that are below a specified threshold amount (either percent of the landscape unit, or area).
The option of Target number of HRUs limits the number of HRUs in the whole watershed to a user preferred amount (i.e. between the lower limit of one HRU per landscape unit and the upper one of retaining all potential HRUs).

## Slide 54
1.4 HRU definition
Filter by area
If Filter by area is chosen there is then a choice of threshold method, and a choice of threshold value.
If the method chosen is Percent of landscape unit and the value (set by moving the slider or typing in the box) is, say, 10, then HRUs which are less than 10% of their LSUs will be removed.
If the method chosen is Area (ha) and the value set is, say, 5, then HRUs which are less than 5 ha will be removed.

## Slide 55
1.4 HRU definition
Setting a target
If Target number of HRUs is chosen there is then a choice of threshold method, and a choice of target value.
Suppose, for example, we set a target of 250 HRUs, out of the current 455.
If the method chosen is Percent of landscape unit then the HRUs will be sorted in order of their percentages of their LSUs, and the smallest 205 will be eliminated.
If the method chosen is Area (ha) then the HRUs will be sorted in order of their areas in hectares, and the smallest 155 will be eliminated.
Targets are typically exceeded when exemptions for some landuses have been chosen, or landuses are split, as splitting is done after elimination. If the result has too many HRUs you can always run again with a lower target.

## Slide 56
1.4 HRU definition
Filtering by landuse, soil and slope
For this exercise we will use Filter by landuse, soil, slope. Select this option, and choose Percent of landscape unit as the method.
We will first set the landuse percentage to 10 and click Go. This means for each LSU we will not include any landuse for which the percentage area in the LSU is less than 10. The number 51 at the end of the landuse slider indicates that this is the lowest percentage for a dominant landuse across all the LSUs. Trying to set the percentage higher than this would mean trying to remove all HRUs from at least one LSU.
We set the same percentage of 10 for soil and click Go, and also for slope. Then we complete the HRU selection by clicking Create HRUs.

## Slide 57
1.4 HRU definition
HRUs report
There is then a Ground water option which enables users to use the new gwflow module, but in this exercise we will use the default option SWAT+ aquifers not to.
We see in the main QSWAT+ form, under Select report to view, that there is a new report available: HRUs
This shows the detailed actual and percentage areas for the watershed and each subbasin, for each landuse and soil, before and after HRU creation, and for each HRU.
If you want to change the HRU thresholds and selection, click on Create HRUs in the main QSWAT+ form to reopen the Create HRUs form. Read choice will be set to Read from previous run, and you can click Read and redo HRU selection.

## Slide 58
1.4 HRU definition
Actual HRUs
Create HRUs is now reported as done and the third step is enabled
A shapefile Actual LSUs has been added and, if you requested a Full HRUs file (as we did) an Actual HRUs shapefile has also been added.
These contain the actual LSUs after any channel merges, and the potential HRUs that were retained as actual HRUs that is simply the Full HRUs file with the eliminated HRUs removed.

## Slide 59
1.4 HRU definition
Actual HRUs
It appears from the Actual HRUs file that there are now holes in the watershed. But in fact the retained HRUs have been proportionately increased in size so that in each subbasin their total area is the area of the subbasin. This can be seen from the before/after figures in the HRUs report.
The actual LSUs shapefile attributes table shows the LSU identifiers, the channel and the subbasin. The actual HRUs shapefile attribute table shows the subbasin and channel, the landscape category, (original) landuse, soil, and slope band, and the HRU number(s)
In the case of split HRUs there can be more than one HRU number for a shape, as it is impossible to show in a shapefile the splitting by arbitrary amounts of the original potential HRUs.

## Slide 60
1.4 HRU definition
Actual HRUs
A new shapefile has been added, title Channel reaches. This is formed from the channels shapefile created during delineation, but has channels merged.
Another shapefile, showing the point sources that are automatically added to each channel, and any reservoirs that were added, has also been added. A point source is added to every channel as a convenience because users can add data (in the SWAT+ Editor) for any point sources they want to include in their model

## Slide 61
1.4 HRU definition
Actual HRUs
You are now able to click the Edit Inputs and Run SWAT button to start the SWAT+ Editor, set the rest of the parameters and input data you need, and run the SWAT+ model.

## Slide 62
1.5 SWAT EDITOR
Setting up the Robit example in the SWAT Editor
Before starting, you can prepare weather generator information. The Robit example data includes such data in the Robit directory, and no more preparation is required.
Second you will need (if you have it) to supply observed weather data. The Robit example data includes such data, in Robit/ClimateRobit, and no more preparation is required.
After starting the editor, click Start to import the project and reference databases.

## Slide 63
1.5 SWAT EDITOR
Weather data
Then on the project summary screen click Get started, and then on the next screen Add weather generators now.

## Slide 64
1.5 SWAT EDITOR
Weather data
To set up the weather generator, click Import data and select Two CSV files as the data format.
Browse to Robit/WGEN_Robit_stat.csv as the Stations csv file, and Robit/WGEN_Robit_mon.csv as the Monthly values csv file. Check the box to state that you have observed weather data and click Import data.

## Slide 65
1.5 SWAT EDITOR
Weather data
The weather data generator data is imported and you will see a single row since there is only a single station in this data

## Slide 66
1.5 SWAT EDITOR
Weather data
With the weather generator set up, select Weather stations at the top left. In the Weather Stations form click Import data. The Robit observed data is in the SWAT2012 format, so leave this as the choice in the first box. For the weather files directory, browse to select the folder Robit/ClimateRobit. For a directory to save the files you can choose anywhere you like, but the default of the Scenarios/Default/TxtInOut folder, where other input files will be stored, is a sensible choice. Click Import Data

## Slide 67
1.5 SWAT EDITOR
Weather data
The Weather Stations form will reappear, showing a single station with data for precipitation, temperature, solar radiation, relative humidity and wind speed

## Slide 68
1.5 SWAT EDITOR
Simulation period
Click the triangular symbol on the left for Run SWAT+, which opens the simulation settings page

## Slide 69
1.5 SWAT EDITOR
Simulation period
Under simulation settings the folder for the SWAT+ input files can be left as the default. Select Set your simulation period.
We have daily data for the beginning of 1990 to the end of 2013, but to keep down the time needed to run and to import the output data we will restrict the period to 1990 to 2000. Use the date picker to change the ending date to 31 December 2000.

## Slide 70
1.5 SWAT EDITOR
Print options
Select Choose output to print. We will use 3 as the warm-up period. SWAT+ will run for the first three three years, but the output will be ignored.
For the objects to print, some output is preselected. We will visualise a variety of outputs, so select just three of the top boxes under Monthly, Yearly and Average. Then find and add channel under Daily, which we will need for calculating environmental flows. We won't include other daily output as it will take some time to write nearly 3000 records for each channel, lsu or hru in requested output

## Slide 71
1.5 SWAT EDITOR
Run SWAT+
Scroll down and make sure Write input files, Run SWAT+, and Analyze output for visualization are all checked. We don't need the debug version, which you would normally only use if the model has errors, to get more information.
Click Save Settings & Run Selected. We see the input files being written, then SWAT+ running, and the output files being read. They are being stored in an output database, swatplus_outputs.sqlite in the Scenarios/Default/Results folder.
We selected a lot of outputs, so this takes a few minutes. When it is finished we can Exit SWAT+ editor.

## Slide 72
1.6 Output Visualization
Visualisation
Once SWAT+ has been run and the output imported, so that there is an output database swatplus_output.sqlite in the Scenarios/Default/Results directory of the project, then a button Visualise becomes available in the main QSWAT+ form. Visualisation allows outputs from SWAT+ to be visualised graphically.

## Slide 73
1.6 Output Visualization
Running Visualise
Click Visualise on the main QSWAT+ form to bring up the Visualise Results form.
Here the Choose scenario pull-down menu shows the simulations, or scenarios, that are available, currently only the Default one. Select the one that you wish to display.
Then use the Choose SWAT+ output table to see what tables are available.

## Slide 74
1.6 Output Visualization
Visualisation period
The start and finish dates shown are initially the start and finish dates of output from the Default scenario.
Note that the initial year is 1993 since we simulated from 1990 but set warm-up period (nyskip) to 3. You may choose dates within these if you wish, to shorten the period being visualised.
If other scenarios are selected, the dates will be changed if necessary to ensure there is data available for the whole period.

## Slide 75
1.6 Output Visualization
Visualisation type
There are four possibilities shown by the tabs for Static data, Animation, Plot and Post Processing.
For static data a single summary value (such as a mean or a maximum) is calculated for each aquifer, channel, HRU or LSU and displayed as a map.
For animation there is an animated display of the value in each aquifer, channel, HRU or LSU at each time step in the animation.
Plot supports the creation and display of graphical plots of selected variables.
Post processing helps us calculate a number of environmental flows.

## Slide 76
1.6 Output Visualization
Visualizing Statistic Data
Select the Satic maps tab
Static results are created by generating a shapefile, and by default this will be called <table>results.shp (e.g. lsunit_pw_monresults.shp) and stored in the Results directory of the current scenario. You can change the file name and/or location if you wish.
Select lsunit_pw_mon as the SWAT+ output table.
The pull-down menu in Choose variables contains all the output variables from your chosen table. You can select these one at a time and use the Add button to add them to the box below, or simply click All to get all of them. You can adjust your selection by selecting and using Del to delete ones, or using Clear to delete all of them.
Data from all the variables you place in the box will be placed in the results file. You then need to select one of them to be displayed. It is a good idea in general to select All as this allows you to display different variables without having to change the results file

## Slide 77
1.6 Output Visualization
Visualizing Statistic Data
For each variable, for each aquifer, channel, LSU or HRU the output data can have a value for each day, month, or year of your simulation, or an average year for the whole simulation
To display the results graphically we need to produce a single value for each variable for each subbasin, and for this we choose a Summary. Summaries available are:
Totals means, for each subbasin, a total value across the simulation
Daily, Monthly, and Annual means are averages: the total figure divided by the number of days, months, or years respectively in the simulation.
Maxima and Minima are the maximum or minimum values of the variable in the simulation.

## Slide 78
1.6 Output Visualization
Visualizing Statistic Data
We need to select a variable to display. Select bioms.
Select Monthly means in summary and click Create
The shapefile is created on the map and the text in the map canvas shows that we are displaying bioms monthly mean values from the Default simulation

## Slide 79
1.6 Output Visualization
Visualizing Statistic Data
The results layer is given a default colouring using 5 intervals chosen by the Jenks natural breaks algorithm to cover the range of summary values for the variable. You can change the colouring scheme if you wish (right click on the layer entry in the Layers panel, select Properties and then select the Symbology tab)
To display a different variable from the list, select it with the mouse and click Create. To change the summary, select the new one from the pull-down menu and click Create.
We chose an LSU results table, so it was displayed by colouring LSU shapes. HRU output colours HRU shapes. Results from channels are displayed using channels.. The thickness of the channel shapes is proportional to the channel width.
Also, if you calculate a new field in the Field Calculator, you will find the new field name(s) added to the variables that can be selected for display.

## Slide 80
1.6 Output Visualization
Printing
QSWAT+ provides templates to create a composition of 1, 2, 3, 4 or 6 results maps layout in either landscape or portrait mode.
QSWAT+ uses the QGIS Print Composer to support the printing of results. Indeed, you can edit the templates to change text, change the size and position of maps, etc.
Each template includes as well the maps and legends:
Page title
North arrow
Scale bar
Text box containing Author/Company
Date

## Slide 81
1.6 Output Visualization
Printing
We' ll make a 3-map display, adding two more static results files to the display:
Switch to the lsunit_ls_aa table and create the sedorgn map
Switch to the channel_sdmorph_mon table and create the maximum peakr map.
Select Portrait as the orientation and 3 as the number of maps, and clicking Print
The print composer is started and shows the first 3 (in this case) maps in the Results group in the layers panel, regardless of their current visibility.
Visible layers in the Watershed group are included as background

## Slide 82
1.6 Output Visualization
Printing

## Slide 83
1.6 Output Visualization
Printing
The items in the print composer can be edited. You may want to change the title from its default of SWAT+ results: <project>, to edit the Company/Author box appropriately, change the map scales, adjust their positions, add other items, etc.
You can then export it as an image, pdf or svg file.
To scale several maps, select the Item Properties tab, click on one map item, which forms a box round it. Drag a corner of the box to change the scale. Note the scale number. Then change the others to the same scale, this time by editing the number and pressing Enter for the change to take effect.
The scale bar is attached to the top left map, so it changes with it.
You may also need to use the Position and size settings further down under Item properties to keep the maps aligned.

## Slide 84
1.6 Output Visualization
Rules for creating print layouts
If n maps are requested, the first n maps in the Results group of the Layers panel are used, regardless of current visibility.
Layers in the Watershed group are included as background if they are currently visible. The Watershed layer is commonly used to provide subbasin boundaries. Results layers have transparency set to 35% so that background layers are visible.
If you want to include, for example, a landuse map, drag it into the Results group before clicking Print.
The map layers in the composition are set locked: otherwise they would only show whatever the canvas shows, but they can still be resized or moved.
The scale bar is attached to the top left map. If you change its size the scale bar will adjust, but you need to change the others manually to match.

## Slide 85
1.6 Output Visualization
Printing
When you have finished with a layout, maybe by exporting it as a pdf, closed it and don't want to revisit it, it is a good idea to delete it from the QGIS Layout Manager, since QGIS seems to be sensitive to having more than a very few layouts.
Open the Layout Manager (using Project -> Layout Manager), select the layout in the manager panel, and click Remove.
Or, if you have closed but not removed a layout, you can open it again using the Layout Manager's Show button.

## Slide 86
1.6 Output Visualization
Animation
To animate, after choosing the scenario and the SWAT output table (e.g. channel_sdmorph_mon), select the Animated maps tab.

## Slide 87
1.6 Output Visualization
Animation
Select New in the Set up animation group
There are two modes of animation: map canvas and print composer. We will use now the map canvas.
The Variable pull-down menu contains all the variables from the chosen output table: select one of these (e.g. flo_out).
A new animation layer is created in the map canvas, showing the initial values of this variable in the simulation
Note that the range of possible values runs from the minimum and maximum values for flo_out for the whole simulation period.
You can view the actual initial values for each channel by examining the attribute table

## Slide 88
1.6 Output Visualization
Animation

## Slide 89
1.6 Output Visualization
Animation
There are controls to run, pause and rewind the simulation: it steps through daily, monthly or annual time steps according to the chosen table. The speed of the animation can be adjusted using the Speed spinbox.
You can also investigate the changing values manually, by dragging the slider, or (with the Visualise Results form the currently selected window) by pressing the left and right arrows on your keyboard.
The date (day, month, or year) of each step appears above the slider.

## Slide 90
1.6 Output Visualization
Animation
The animation is achieved by creating a shapefile, in this case rivs0.shp in the Animation directory within the Results directory of the scenario.
At each time step the values of the variable are updated and the file redisplayed. Hence this file is being continuously changed.
It is regarded as a temporary file and so is not preserved. If you wish to save a view of the animation at a particular moment you can pause the animation and make a copy of this file

## Slide 91
1.6 Output Visualization
Animation Recording
It is also possible to make an animated gif of the animation.
Click the green Start recording button before running the animation, and then the red Stop recording when it reaches the end (or whenever you like).
You will be informed (after a pause while the file is created) that the animated gif has been created (called <variable>Video.gif in the Results directory).
Click OK to accept the message, and then click Play to see it run in whatever is the default player for animated gifs on your machine. Animated gifs can also be played in web browsers.
The speed of the animated gif is determined by the value in the speed spinbox when the Stop recording button is pressed, so you may run it at one speed, wait for it to finish or press pause, and then change the speed before you click Stop recording.

## Slide 92
1.6 Output Visualization
Animation Recording
Each step in the recording has been saved as a PNG file. When you stop recording the PNG files are assembled into an animated GIF.
The animated gif is made by saving a .png file at each time step in the Results/Animation/Png directory of the Default scenario.
These files are deleted when Stop recording is clicked, so if you want to use them, perhaps to make your own animation, you need to copy them before you stop recording.

## Slide 93
1.6 Output Visualization
Animation with Print Composer
If we want to animate more than one variable at once the map canvas is not very suitable as the animations will overlay each other. So we can use a print composition.
Even for a single animation the print composer offers more options fo setting the title, author, scale bar etc. This may be recorded if desired.
Keep the New setting (if you choose Current the next animation will replace the old one). Change the table to lsunit_wb_mon and select surq_gen as the variable.
Select Print Composer as the Animation mode.
Select Landscape and 2 as the number of maps. This selects the first 2 maps in the Animation group, regardless of visibility.

## Slide 94
1.6 Output Visualization
Animation with Print Composer
Move the slider by hand towards the end of the period, e.g. June 2000 to reduce the number of images
Click Start recording. A form explains that the composer will start, and you can modify it, but you must then save it as AnimationTemplate.qpt in the Results folder of the Default scenario. Click OK and the composer appears

## Slide 95
1.6 Output Visualization
Animation with Print Composer
Make any changes you wish in the print composer
Use Layout -> Save as Template to save it as ….\Robit\Demo\Scenarios\Default\Results\AnimationTemplate.qpt as instructed. Confirm overwriting, and Quit the print composer.
The red start/stop button indicates that recording is ready to start. Click the play arrow.
The composer is used to generate an image for each time step. It runs slowly as it creates a layout and saves it as a .png file at each time step. When it finishes, click Stop recording. A message tells you where the recording is stored - as Videon.gif (n is a number) in Default\Results.
Click Play to see the saved animation.
As with static visualisation, it is possible to change the colouring scheme used (the colour ramp and/or the number of classes)

## Slide 96
1.6 Output Visualization
Plotting
Plotting allows the rapid display of output data as line graphs or bar charts, plotting values against time. It is intended to facilitate comparisons of outputs from different scenarios, or different aquifers, channels, LSUs or HRUs, or between simulated and observed values.
Plotting is done in two stages, data collection and display. After collection, just before display, data is saved in a comma-separated value (.csv) file. This file can be loaded into tools like Excel to support more extensive analysis than provided by the plotting tool SWATGraph that is supplied with QSWAT+
We are going to compare simulated output from our main outlet with observed data which we have.

## Slide 97
1.6 Output Visualization
Plotting
Select the Plot tab
Choose our observed data file, which is Robit\Observed\observedFlow.csv
You can start by making sure an output table is selected, e.g. channel_sd_mon, and clicking Add plot.
This adds a row to the table, and already shows the chosen scenario and table. The Unit field is empty and so is the Variable.
This first row is also the currently selected row, and this is important. Whenever we change the scenario, output table, unit or variable settings through their pull-down menus we will immediately change values in the currently selected row. When you have more than one row you can select a row by clicking in it.
We select flo_out as the Variable

## Slide 98
1.6 Output Visualization
Plotting
The units will be channels, and to complete the table we need to find the channel number of the outlet channel.
There are several ways of doing this.
When we use the Unit pull down menu, as each potential choice is highlighted when we move the mouse over it, the corresponding channel, is highlighted in the map canvas.
We make sure that the Show Map Tips QGIS button is pressed, select the appropriate map in the layer panel (rivs1) and hover the mouse over the feature. A map tool tip will be displayed showing the unit type (e,g, Channel) and number.
We select the appropriate map in the layers panel, as in the previous method 2. We click the Identify Features QGIS button and click on the intended feature, such as the outlet channel. We see from the Identify Results panel that the channel number is 1, so we select 1 as the Unit.

## Slide 99
1.6 Output Visualization
Plotting
If we had a different run in another scenario, and wanted to compare, we would now use Copy plot, which copies most of the entry above, change the scenario (top of the form), and set the channel to 1;
Note the way that changing one of the pull-down menus changes the currently selected plot entry.
Since we don’t have a different scenario, we remove the extra entry with Delete plot.

## Slide 100
1.6 Output Visualization
Plotting
Click Add observed to add an entry from our observed data file. It uses observed as the name of the scenario, '-' is used for Table and Unit and allows us to choose the data column from those in the file.
In this case there is only one, Flow, and so it is preselected.
Set the Plot type to Graph/bar chart. (We describe other plot types later.) Then click Plot.
This invites us first to choose a .csv file to save the data. We can if we wish later import this into, for example, Excel if we wish to do further manipulations or use Excel’s graphing tools. Provide a name, e.g. flow, and click Save.

## Slide 101
1.6 Output Visualization
Plotting
You will get an error saying the data for 1998/1 is missing for the second plot, the observed one.
Our observed data only runs from January 1993 to December 1997.
Change the year of the finish date to 1997 and click Plot.
Choose the same output file name, and confirm you are happy to overwrite it.

## Slide 102
1.6 Output Visualization
Plotting
Once the data is written to the .csv file, SWATGraph is automatically started to display the data graphically. The data has been displayed as line graphs.
We can change the display to bar chart using the Chart Type pull-down box and clicking Update. The graph shows a plot of the flow out of channel 1 against the observed data file observedFlow.csv

## Slide 103
1.6 Output Visualization
Plotting
Other SWATGraph options include importing another (similarly created) .csv file, using New File to Plot, and using the buttons immediately below the graph.
These include zooming and panning the graph, saving the graph in a variety of image formats (the rightmost button) and a number of editing options (rightmost button but one).
You can add a title, change axis labels, change the colours of the plots, and (for line graphs only) change the vertical axis from linear to log scale, which is useful when there is a wide variation in values.

## Slide 104
1.6 Output Visualization
Plotting
The data from the model and from .csv file is also displayed. The column headings, also shown in the graph legend, take the form Scenario-Table-Unit-Variable(Units), where Unit is the aquifer, channel, LSU or HRU number as appropriate for the table, and Units is the units in which the Variable is measured..
In this example is Default-channel_sdmorph_mon-1-flo_out(m^3/s)
For an observed plot the form is observed-Variable.
In this example observed-Flow
At the bottom of the screen some statistics are displayed. These are correlation coefficients and Nash coefficients for each pair of plots.

## Slide 105
1.6 Output Visualization
Plot types
A number of plot types are supported:
Line graphs/bar charts
Flow/load duration curves
Scatter plots
Box plots
The type can be selected from the Visualise Results form, as we saw earlier, before starting SWATGraph, or from the Plot type pull-down menu in the SWATGraph form.

## Slide 106
1.6 Output Visualization
Plot types
We can add the variable sed_out for channel 1 from the channel_sdmorph_mon table and using plot type Duration curve. This illustrates another feature of the line graph and duration curve plots that when the variables are different extra axes are added on the right, showing the appropriate range of values for each additional variable.
The colour of the axes matches the colour of the (first) graph for that variable. There is no need for an axis for the observed data because it is assumed to match the variable of its immediately preceding graph, that for flo_out.

## Slide 107
1.6 Output Visualization
Plot types
Change the SWATGraph plot type to Box plot.
There is a box plot for each data set, and those sharing the same variable are grouped together.
Numerical values for each box plot (minimum, maximum, median, lower and upper quartiles) are included in the bottom panel.

## Slide 108
1.6 Output Visualization
Plot types
To illustrate scatter plots we Close SWATGraph, delete the observed data line in the plot table, so we are left with the flo_out and sed_out lines, and select Scatter plot as the type.
Plotting shows the line of best fit as well as the scatter points.

## Slide 109
1.6 Output Visualization
Observed data
Observed data is essentially a comma-separated-value file (.csv) with:
Headings on the first line, separated by commas
As many data values as there are headings on each succeeding line, separated by commas
As many data lines as there are dates in the SWAT+ output.
If the first heading is DATE (or date, Date, or the same 4 letters in any cases) then the first column is ignored. It is assumed (and not checked) that the dates correspond to the dates in the SWAT+ output.
Leave blank for missing data, or put any text which cannot be parsed as a number, e.g. 'missing'. Missing data will be omitted from graph.

## Slide 110
1.6 Output Visualization
Post Processing
Post processing of SWAT+ results is available via the Visualise form, under the tab Post processing.
Three environmental flow statistics are available, Qq, dQp and Qb.
Calculation of these statistics depends on data in the channel_sdmorph_day table in the outputs database, so channel in the Daily column must have been be selected amongst the outputs to be printed by the SWAT+ Editor.

## Slide 111
1.6 Output Visualization
Qq statistic
Qq provides for each calendar month the flow in m³/s that is exceeded by q% of the flows in that month.
The user chooses the subbasin and the value of q.
For example, if you set q to be 95%, and set the subbasin to 7 (outlet subbasin), and the August result is 0.03, then 95% of the time the average daily flow from subbasin 7 in August is at least 0.03 m³/s

## Slide 112
1.6 Output Visualization
dQp statistic
The dQp statistic provides a single flow statistic for a given subbasin, where d is the number of days for a moving average, p is a threshold percentage. 21 is the default for d, 5 for p, and the watershed outlet subbasin for the subbasin.
Users also need to choose a start month and can choose between Percentile and Mean as the final statistic selection. The statistic is a flow in m³/s.
Percentile: The result is the flow value which is not exceeded by p% of the flows for the year periods. For the default settings, the result would be called 21Q5.
Mean: The result is the mean of the flows for the year periods. For the default settings the result would be called 21Qm. Note that the value of p is ignored.

## Slide 113
1.6 Output Visualization
Qb statistic
Qb, The Basic Flow statistic provides an annual and also monthly statistics for a selected subbasin. A rate of flow for each year is calculated as the minimum moving average for a year, where the length of the moving average is chosen as the one that gives the highest rate of change between the minimum and the previous moving average. The annual result is then the mean of these flows for each year.
The values for each month are the annual result multiplied by the variation factor for the month. The variation factor is calculated as the square root of a ratio, the ratio of mean daily flow for days in that month to the minimum such figure for all months.

## Slide 114: Thank You
Notes: Click on the graphical edit button.
Press the Single-Point Edit tool.
Find the new value of the point on the graph that you want to edit and double click the mouse at that location. A magenta triangle will appear in that location and a value will appear in the corresponding row in the estimate entry column.
Press the curve edit tool
Draw a curve in the graph (right click for the final point). A series of magenta triangles will appear in the new desired values and simultaneously the corresponding Estimate/Entry cell will be modified.
Press the Accept button or the Accept All button to accept all edits. This will copy the data from the Estimate/Entry column into the Revised column.
At the end of all of your edits, press the Save or Save As button.