## Slide 1
Consultancy service for the Development of the Eastern Nile Water Resources Models and Tools
Nile Cooperation for Climate Resilience
Eastern Nile Technical Regional Office (ENTRO)
Validation Workshop
12-14 June 2025

## Slide 2
Methodological approach
Schematization of the integrated approach pursued by the Consultant

## Slide 3
Time (hrs) | Presentation / Activity | Responsible Person
 | June 14, 2025 - Day 3 | Chair: To be assigned
09:00 –09:10 | Recap of Day 2 | HydroNova/ ENTRO
09:10- 10:00 | Presentation on WP2: Water resources planning model | HydroNova (Consultant)
10:00-11:00 | Interactive session on water resources planning model | All
11:00 – 11:30 | Health Break | Hotel
11:30-12:00 | Presentation on WP3: Sediment and erosion transport model (HEC-HMS) | HydroNova (Consultant)
12:00-13:00 | Interactive session on Sediment and erosion transport model (HEC-HMS) | All
13.00 – 14:00 | Lunch Break | Hotel
14:00 – 15:00 | Presentation on WP3: Sediment and erosion transport model (SWAT) | HydroNova (Consultant)
15:00-16:00 | Interactive session on Sediment and erosion transport model (SWAT) | All
16:00-16:30 | Health Break | Hotel
16:30- 17:00 | Feedback and recommendations on WP3 | All
17:00-17:30 | Closing remarks and a way forward | ENTRO/ENSAPT
Workshop Agenda

## Slide 4
Specific Topics
DAY 3. WP3 – HEC HMS SEDIMENT
Introduction | 
Data Sources and retrieval | Available sediment data Soil Database DTM Land cover Scenarios
Calibration | Method Results
Simulation | Scenario 0 Scenario 1 and 2

## Slide 5
WP3 – Sediment and erosion transport models development
HMS models development
Introduction
Watershed erosion and sediment routing
(HEC-HMS)
Watershed erosion and sediment routing
(HEC-HMS/SWAT)
GIS sediment/erosion mapping
QGIS
Reservoir sediment trap
(EXCEL)
Reservoir sediment trap
(EXCEL)

## Slide 6
WP3 – Sediment and erosion transport models development
HMS models development
Introduction
In series to the hydrological model, the sediment/erosion model has been added.
INPUT
MODEL
OUTPUT
Boundary Conditions:
Rain
ET
DEM
HEC-HMS
Surface sediment load
Initial Conditions:
Canopy
Surface
Loss
Baseflow
Transform
Routing
Erosion on subcatchments
Tranport on reaches
Observed
Sediment Load
CALIBRATION
COMPARISON

## Slide 7
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Available sediment data
The available information on sediment dynamics within the project basins is fragmented and characterized by low reliability and consistency.
Only for the Blue Nile Sub-basin.
The records are discontinuous: in many cases just a few data is missing, while in others, measurements are limited to a few scattered days per year.
Some datasets lack units of measurement.
Certain sediment load values appear inconsistent when compared to their reported units or the concentration in PPM.
Most data points are concentrated in the summer and autumn months, corresponding to peak river flow conditions. As a result, they cannot be considered representative for calibration over the entire year.

## Slide 8
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Available sediment data
Reliable data |  | concentration |  | load | 
Blue Nile at Bahir dar | scattered data from 1961 to 1996 | 502 | mg/l | 3932 | t/day
Blue Nile at Wad El Ais | 10 oct 2001 - 10 nov 2001 | 434 | ppm | 66.65 | 10^3 t/day
Rahad at Hawata | 21 jul 2001 – 18 oct 2001 | 373 | ppm | 4.244 | 10^3 t/day

## Slide 9
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Available sediment data on reservoirs
Roseires dam was constructed in 1966 and had an initial trap efficiency estimated at 79%, dramatically reduced over the year
Assuming a correct gate sluice operation, the Sennar dam (1925) trap efficiency can be estimated as about 25%.
In general, trap efficiency is highly dependent on
operational decisions, which can significantly influence sediment retention and transport dynamics, in addition to
the capacity/inflow ratio: higher ration correspond to higher retention.

## Slide 10
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Soil database
Harmonized World Soil Database by ISRIC.
The HWSD2 has been used as a source for most of the parameters in the sedimentation analysis in HMS
https://data.isric.org/geonetwork/srv/ita/catalog.search#/metadata/54aebf11-ec73-4ff8-bf6c-ecff4b0725ea

## Slide 11
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Soil database
Harmonized World Soil Database by ISRIC.
Soil is divided into units.
Characteristics needed:
Sand, silt, clay percentage
Bulk density
Organic carbon content

## Slide 12
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Soil database – sand, silt, clay percentage

## Slide 13
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Soil database – sand, silt, clay percentage

## Slide 14
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Soil database – organic content and organic matter
Percentage of organic matter, calculated as OM=OC⋅1.724, where OC is the organic carbon (% weight) available in the HWSD2

## Slide 15
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Soil database – bulk density and permeability class
Bulk Density (g/cm3) | Permeability Class | Description
<1.0 | 6 | Very High
1.0−1.2 | 5 | High
1.2−1.4 | 4 | Moderate
1.4−1.6 | 3 | Moderately Low
1.6−1.8 | 2 | Low
>1.8 | 1 | Very Low

## Slide 16
WP3 – Sediment and erosion transport models development
Data sources and retrieval
DTM – FLOW ACCUMULATION AND SLOPE
long slopes have more erosion than short slopes
steep slopes have more erosion than flat slopes

## Slide 17
WP3 – Sediment and erosion transport models development
Data sources and retrieval
LAND COVER
Land cover classification gridded maps from 1992 to present derived from satellite observations
This dataset provides global maps describing the land surface into 22 classes, which have been defined using the United Nations Food and Agriculture Organization’s (UN FAO) Land Cover Classification System (LCCS)

## Slide 18
WP3 – Sediment and erosion transport models development
Data sources and retrieval
LAND COVER

## Slide 19
WP3 – Sediment and erosion transport models development
Data sources and retrieval
LAND COVER
The cover factor describes the influence of plant cover on surface erosion. Bare ground is the most susceptible to erosion while a thick vegetation cover significantly reduces erosion. Typical values range from 1.0 for bare ground, to 0.1 for fully mulched or covered soils, to as small as 0.0001 for forest soils with a well-developed soil under a dense tree canopy

## Slide 20
WP3 – Sediment and erosion transport models development
Data sources and retrieval
LAND COVER
Example of Land cover classification for a subcatchment in the Atbara basin
A weighted average is calculated based on the area of the cover factor associated with the different land cover classes. Thus, a single cover factor is obtained for each sub-catchment

## Slide 21
WP3 – Sediment and erosion transport models development
Data sources and retrieval
Scenarios – Climate Data Storage (Copernicus)
Scenarios involves meteorological conditions and are the same of the hydrological simulations.
Scenario 0 – Current conditions: Rainfall and temperature for evaporation calculation are derived from ERA5 data portal, as agreed in the previous phases of the project, for the time window 1972-2023.
Scenario 1 – 2060 – SSP2-4.5: Rainfall and temperature used in scenario 0 impacted according to seasonal forecast and to subbasin spatial forecast, according to SSP2 scenario.
Scenario 2 – 2060 – SSP3-7: Rainfall and temperature used in scenario 0 impacted according to seasonal forecast and to subbasin spatial forecast, according to SSP3 scenario.

## Slide 22
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion
In addition to the hydrological methods already described yesterday, there are also methods related to sedimentation and erosion
Soil erosion
Stream
Erosion
Transport
Sediment
Reservoir
sediment
Erosion on the subcatchments

## Slide 23
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion
When water flows over the land surface and through stream channels, it significantly impacts the landscape through various processes:
Soil erosion: Shallow surface flow erodes soil, transporting sediment overland to headwater streams.
Streambed erosion: In steep headwater streams, high flow velocities lead to the erosion of the streambed.
Sediment transport: Eroded soil and bed material are carried downstream by the flow, moving sediment to lower reaches of the watershed.
Streambed deposition: As flow velocity decreases in the lower reaches, sediment is deposited. Reservoirs within the watershed can trap some or most of the incoming sediment

## Slide 24
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion – Global properties
The Sediment Transport Potential Functions define the method used to calculate the sediment-carrying capacity of streamflow for non-cohesive sediments.
Sediment Delivery Ratio (SDR) Transport Potential method:
SDR = equilibrium
SDR < 1 sediment retention
SDR > 1 erosion
Clay remains in suspension, while silt, sand and gravel are in equilibrium
Default parameters
Properties that apply globally to all elements in the basin model

## Slide 25
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion – sub-catchment erosion
Modified USLE approach
Rain drops cause erosion when they impact the ground surface and break apart the top layer of the soil,
dislodging soil particles to move with the overland flow.
Overland flow also imparts an erosive energy to the ground surface that may further break apart the top soil layer.
As the overland flow rate increases, the flow becomes concentrated in rills which focuses erosive energy and further erodes the surface.
Total erosion is closely linked to precipitation rate, land surface slope, and condition of the surface. In some cases, soil eroded high in the catchment may deposit before reaching the outlet of the subbasin

## Slide 26
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion – sub-catchment erosion
Modified USLE approach
The sediment Yield is calculated based on some parameters:
Erodibility factor  Soil database
Gradation curve  Soil database

## Slide 27
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion – sub-catchment erosion
Modified USLE approach
The sediment Yield is calculated based on some parameters:
LS = topographic factor  DTM, adjusted in phase of calibration
C = cover factor  Land cover
P = practice factor  calibrated parameter
Threshold and exponent  calibrated parameter

## Slide 28
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion – reach transport
Uniform equilibrium method
The Uniform Equilibrium Method simplifies sediment transport calculations by assuming that sediment moves through the reach without delay, making it a straightforward approach within sediment routing modeling.
Parameters:
Gradation curve: it assumed to be the same of the sub-catchments

## Slide 29
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion – reservoirs sediment trap
Sediment trap
In the reservoirs, where there is minimal horizontal water movement, sediment particles gradually lose their buoyancy and settle to the reservoir's bed. Over time, the cumulative loss of storage space due to sediment accumulation can become substantial.
The river network of the two basins under study for WP3, Blue Nile and Atbara, is impaired by the following reservoirs:
Reinassance, Roseires and Sennar for the Blue Nile;
Tekeze, Upper Atbara Project, Khashm El Girba for Atbara

## Slide 30
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion – reservoirs sediment trap
the impact of the reservoirs on sediment load in the reaches was evaluated manually externally from the models developed, to provide an average estimate of the annual sediment load.
In literature sediment traps depends on
C/I = Capacity/Inflow Ratio
Brune approach, best fit with the observed data
Chart: Comparison os fediment Trap Efficiency models
| 7.0000000000000001E-3 | 0.02 | 0.03 | 0.05 | 0.1 | 0.16 | 0.3 | 0.4 | 0.5 | 1 | 2 | 3 | 4 | 5 | 6 | 10
TE - Brune (minimum) | 17.8555 | 39.165 | 46.8411 | 55.6337 | 65.4661 | 70.5352 | 75.2803 | 76.7505 | 77.6322 | 79.2553 | 79.8295 | 79.94 | 79.974 | 79.9872 | 79.9931 | 79.999
TE - Brune (medium) | 34.3708 | 59.0906 | 67.4449 | 76.5517 | 85.9752 | 90.3979 | 94.1266 | 95.1609 | 95.7404 | 96.684 | 96.9458 | 96.9844 | 96.9943 | 96.9975 | 96.9988 | 96.9999
TE - Brune (maximum) | 48.5553 | 71.8485 | 79.1232 | 86.5865 | 93.6122 | 96.5492 | 98.7294 | 99.2565 | 99.528 | 99.9103 | 99.9892 | 99.9976 | 99.9993 | 99.9997 | 99.9999 | 100
TE - Syam (β=0.05) | 0.079049 | 8.2085 | 18.8876 | 36.7879 | 60.6531 | 73.1616 | 84.6482 | 88.2497 | 90.4837 | 95.1229 | 97.531 | 98.3471 | 98.7578 | 99.005 | 99.1701 | 99.5012

## Slide 31
WP3 – Sediment and erosion transport models development
Calibration - method
Sedimentation and erosion – reservoirs sediment trap
 | TE - Current condition | TE – SSP2 | TE – SSP3
Reinassance | 79.2% | 79.0% | 78.8%
Roseires | 70.6% | 69.2% | 68.5%
Sennar | 16.4% | 13.5% | 12.1%
Tekeze | 79.3% | 78.9% | 78.5%
Upper Atbara Project | 66.1% | 62.7% | 60.6%
Khashm El Girba | 52.6% | 47.9% | 45.2%

## Slide 32
WP3 – Sediment and erosion transport models development
Calibration - results
Available records cannot be used for a proper calibration but their purpose is to provide an order of magnitude useful for comparison for the models results
Blue Nile at Bahir Dar | observed 1961 - 1996 | calculated 1972 – 2023 (simulation period)
Sediment concentration (mg/l) | 502 | 177
Sediment load (t/day) | 3932 | 3584
Average flow (m3/s) | 118 | 234
Blue Nile at Wad El Ais | observed 10 oct 2001 to 10 nov 2001 | calculated 10 oct 2001 to 10 nov 2001
Sediment concentration (mg/l) | 434 | 110
Sediment load (t/day) | 666500 | 18101
Average flow (m3/s) | 1649 | 1900
Rahad at Hawata | observed 21 jul 2001 to 18 oct 2001 | calculated 21 jul 2001 to 18 oct 2001
Sediment concentration (mg/l) | 373 | 47
Sediment load (t/day) | 4244 | 911
Average flow (m3/s) | 145 | 224
attempts were made to achieve the same orders of magnitude in both the SWAT and HMS models

## Slide 33
WP3 – Sediment and erosion transport models development
Calibration - results
The models are not able to correctly reproduce sediment load. The causes of these differences may include:
Difficulty in obtaining reliable observed data
Hydraulic structures that alter sedimentation dynamics

## Slide 34
WP3 – Sediment and erosion transport models development
Simulation 0 – current conditions
Subcatchment erosion

## Slide 35
WP3 – Sediment and erosion transport models development
Simulation 0 – current conditions
Subcatchment erosion in the Atbara subbasin

## Slide 36
WP3 – Sediment and erosion transport models development
Simulation 0 – current conditions
Subcatchment erosion in the Blue Nile subbasin

## Slide 37
WP3 – Sediment and erosion transport models development
Simulation 0 – current conditions
River transport. Considered the amount of erosion in the subcatchemnt, the sediment trap into the reservoirs and the routing method chosen, the results in the Atbara rivers are:

## Slide 38
WP3 – Sediment and erosion transport models development
Simulation 0 – current conditions
River transport. Considered the amount of erosion in the subcatchemnt, the sediment trap into the reservoirs and the routing method chosen, the results in the Atbara rivers are:

## Slide 39
WP3 – Sediment and erosion transport models development
Simulation 0 – current conditions

## Slide 40
WP3 – Sediment and erosion transport models development
Simulation 0 – current conditions

## Slide 41
WP3 – Sediment and erosion transport models development
Simulation 1 and 2 – future conditions

## Slide 42
WP3 – Sediment and erosion transport models development
Simulation 1 and 2 – future conditions
Chart: HMS - ATBARA RIVER SEDIMENT LOAD
| ATBARA_1 | ATBARA_2 | ATBARA_3 | ATBARA_4 | ATBARA_5 | ATBARA_6 | ATBARA_7 | ATBARA_8 | ATBARA_9 | QASH_1 | QASH_2
HMS - CURRENT CONDITIONS | 1561 | 2156 | 2156 | 805 | 313 | 313 | 325 | 332 | 274
HMS - SSP2 | 2368 | 3174 | 3174 | 1302 | 557 | 557 | 575 | 586 | 330
HMS - SSP3 | 2924 | 3862 | 3862 | 1664 | 1006 | 750 | 772 | 787 | 366
Chart: HMS - BLUE NILE RIVER SEDIMENT LOAD
| BLUENILE_01 | BLUENILE_02 | BLUENILE_03 | BLUENILE_04 | BLUENILE_05 | BLUENILE_06 | BLUENILE_07 | BLUENILE_08 | BLUENILE_09 | BLUENILE_10 | BLUENILE_11 | BLUENILE_12 | BLUENILE_13 | BLUENILE_14 | DINDIR_01 | DINDIR_02 | RAHAD_01 | RAHAD_02
HMS - CURRENT CONDITIONS | 1318 | 13596 | 17684 | 18378 | 21120 | 22377 | 22969 | 4782 | 1407 | 1407 | 1185 | 1201 | 1204 | 1204 | 120 | 23 | 38
HMS - SSP2 | 1505 | 15124 | 20707 | 21511 | 24867 | 26287 | 27070 | 5691 | 1754 | 1754 | 1475 | 1495 | 1498 | 1498 | 137 | 29 | 46
HMS - SSP3 | 1612 | 15974 | 22888 | 23761 | 27527 | 29013 | 29900 | 6345 | 2000 | 2000 | 1680 | 1704 | 1707 | 1707 | 148 | 33 | 51